# Estimation of missing daily weather data

## Introduction
Climate data are useful in several fields of Earth sciences, including hydrology, hydrogeology and agronomy. However, climate datasets are, most of the time, incomplete. This can represent a major hindrance in various applications, such as for hydrological or hydrogeological model simulations that heavily depend on these data.

For example, the method WHAT is using for the estimation of groundwater recharge requires serially complete (no missing data values) air temperature and precipitation daily datasets. The quality of the groundwater recharge assessment made with this technique is highly dependent upon the quality of the weather dataset used. Hence, the development of a reliable and accurate procedure for the gap-filling of daily weather datasets has been made an integral part of the groundwater recharge assessment in WHAT.

A guide for the preparation of gapless weather data series was presented in Section 3.

This section presents a brief literature review on the subject, followed by a detailed description of the method implemented in WHAT for the estimation of missing daily weather data. Finally, an application is presented for the Montérégie Est region, located in southern Quebec, Canada.

## Literature review
Filling the gaps in weather datasets can quickly become a tedious task as the datasets size and number of stations increase. Moreover, it can also become rather complex when aspects such as time-efficiency of the method, accuracy of the estimated missing values, and preservation of the statistical properties of the weather time series (probability distribution and normals) are taken into account. This is particularly true for the estimation of missing daily precipitation data because of their high spatial and temporal variability (Simolo et al., 2010).

The creation of a serially complete weather dataset generally consists in the replacement of missing daily data with estimated values calculated from simultaneous observations at nearby stations. Within-station method, i.e. methods that only use data from the series being filled, have been proven to perform poorly compared to methods based on the use of data from neighboring stations for the reconstruction of daily precipitation time series (Eischeid et al., 1995; Kemp et al., 1983; Simolo et al., 2010).

Numerous spatial interpolation techniques exist for handling missing data in the weather time-series of a given station that are capable of? using data from irregularly spaced neighboring stations (e.g., simple arithmetic averaging, inverse distance method, single best estimator and multiple regression analysis). Eischeid et al. (2000) found that the multi-linear regression (MLR) method (DeGaetano et al., 1995) usually outperformed six commonly used techniques while testing the creation of serially complete daily temperature and precipitation datasets in the U.S.. Similarly, Xia et al. (1999) also found that the MLR method was consistently the most accurate out of the six classical methods tested to estimate missing daily weather data in Bavaria, Germany. One of the advantage that the MLR approach has over many classical methods is that it can indirectly account for local effects, such as topography, land cover, land use and surface water.
However, weighing and regression-based techniques, including the MLR method, all tend to slightly? overestimate the number of rainy days, while heavy precipitation events are systematically underestimated (i.e., the rainfall probability distribution is usually not preserved with these techniques). However, Simolo et al. (2010) have proposed a two-step procedure to modify the MLR method to address these issues.
In recent years, the estimation of missing daily weather data using artificial intelligence techniques have been the subject of many research studies (Abebe et al., 2000; Coulibaly and Evora, 2007; Kashani and Dinpashoh, 2011; Kim and Ahn, 2008; Srikanthan et al. 2005; Teegavarapu and Chandramouli, 2005). Kashani and Dinpashoh (2011) found that these new data-driven methods, more specifically the artificial neural network and the genetic programming techniques, outperformed the classical application of the MLR approach for three different climates in Iran. Artificial intelligence techniques are interesting because, unlike the classical weighing and regression-based methods, they are able to reflect the inherently stochastic nature of natural processes. Nevertheless, Kashani and Dinpashoh (2011) concluded that the MLR method was an appropriate technique as it performed best? among the eight traditional methods tested, for all the weather variables (air temperature, wind speed, relative humidity and precipitation) for different climate conditions (dry to extra humid conditions) (Kashani and Dinpashoh, 2011).

## Description of the method
Although there exist various methods to estimate missing daily weather data that are well covered in textbooks and technical papers, very? few tools to perform this task efficiently and conveniently are available. The implementation of some of the more complex (and often most accurate) methods discussed in the above section can be a troublesome and even daunting task for a research study that is not directly related to the fields of meteorology or geostatistics. Because of time and resource constraints, it could be tempting to handle the problem of missing daily weather data with a simple method that will not provide accurate estimates for the given dataset. For instance, the use of a simple and straightforward? within-station linear approach between two dates to fill gaps in daily air temperature and precipitation is not appropriate for these weather data (Eischeid et al., 1995; Kemp et al., 1983; Simolo et al., 2010).
The method for filling the gaps in the weather time-series of air temperature and precipitation in WHAT is based on the implementation of the classical MLR method presented in Eischeid et al. (2000). The rationales behind this choice was to provide in WHAT a robust, efficient, accurate, and well known method that was well suited to most conditions (e.g. climate, land cover, topography). Based on the literature review presented in section 8.2, this choice appeared to be the best default option for the first version of the software. Since the programming? code for loading and manipulating the entire weather dataset of a given study area is object-oriented, it will be relatively easy to add modifications to the currently available approach, such as the two-step procedure for the MLR method proposed in Simolo et al. (2010) and/or one of the new artificial intelligence techniques that were developed in recent years (Kashani and Dinpashoh, 2011).
In addition to the handling of missing data, WHAT includes cross-validation resampling technique, to conveniently validate and assess the uncertainty of the estimated missing values. This feature represents a valuable tool for quickly assess the performance of the method for a given study area.

 testing the performance of the different methods available to fill data gaps in a future version of the software. The entire gap-filling process used in WHAT is illustrated in the flowchart in Figure X.

### Step 1: Pre-processing
#### Quality Control
Prior to the analysis of climatic time-series, it is important to apply quality control constraintsto ensure that the data do not violate obvious constraints associated with minimum, maximum, and average daily air temperature and daily cumulative precipitation. This step is not included in the gap filling routine per se. It is why it does not appear in the flowchart of Figure 8.1. It is done every time the software scans the ‘‘Input’’ binder for new weather data file and load them into memory (see Section X).
The program will identify irregularities or inconsistencies to insure that maximum, minimum and average daily temperatures are coherent for a given day and that all daily precipitation values are positive. When inconsistencies are detected, the program issues a warning and offers the choice to replace these erroneous values with ‘‘NaN’’, so that they can be estimated by the program from neighboring stations.

#### Station Correlation Assessment
The subsequent step consists in calculating the correlation coefficients between data of the target station and those of the neighboring stations for each of the four weather variables: minimum, maximum and average daily temperatures and daily cumulative precipitation. These coefficients are calculated for the entire time-series for each neighboring station individually. If there are less than 182 synchronous values between the data of the target station and those of a neighboring station for a given variable, the correlation is not computed and a ‘‘NaN’’ value is kept instead.
An alternative approach would have been to calculate the correlation coefficient with a subset of data from the target series centered around the missing value, as it was done in Simolo et al. (2010) for instance. This approach allows for a better representation of the seasonal variations in the relationships between the stations. The downsides include a more complex algorithm to implement and a reduction of the method robustness and efficiency. This alternative would provide, however, a good additional option in a future version of WHAT and its impact on the accuracy of the method should be assessed.
Based on our experience with daily weather data in Canada, the correlation coefficients between time-series of air temperature measurements is generally higher than 0.98 for stations located at a distance of 100 km or less. The relationships for precipitation are much more sensitive to variations in the landscape (land cover, topography, surface water). As a result, correlation coefficients are generally less than for air temperature and decrease more rapidly with the distance from the target station. A value higher than 0.8 is generally deemed acceptable. This threshold is usually reached for stations within 100 km and with an elevation difference of less than 350 m, the default values in WHAT. Data correlation between two stations will generally decreases as the horizontal and vertical distances increase. It is possible to specify a cutoff distance and a cutoff altitude difference for which neighboring stations that fall above these cutoff values are ignored by the program. The default values are set to 100 km and 350 m for the horizontal and vertical distance respectively based on the literature (Simolo et al., 2010; Tronci et al., 1986; Xia et al., 1999).

### Step 2: Filling the Gaps
The procedure for filling the gaps in the weather data includes two nested loops. The external loop, labeled ‘‘Loop A’’ in Figure 8.1, iterates over the time series of four weather variables for the target station. The inner loop, labeled ‘‘Loop B’’, iterates over every missing value in the data series. The process for the estimation of a single missing value is basically a two-step procedure. The first step consists in selecting the data series with the best correlation coefficient. The second step consists in building a MLR model and estimating the missing values. This is described in more details below.

#### Selection of the neighboring stations
The selection of surrounding stations is critically important for the accurate estimation of missing weather data (Eischeid et al., 1995). However, even if stations are well correlated, problems may arise because of synchronized missing values in the target and neighboring weather station datasets. This is illustrated in Table 8.1, where theoretical time-series of air temperature data with a realistic distribution of missing values are presented.
Table 8.1: Example of well-correlated stations with multiple missing data

Target	Neighbors

Day	X	Y1	Y2	Y3	Y4
1	11.0	12.0	12.0	12.5	10.0
2	nan	12.0	nan	13.0	12.2
3	7.5	8.5	8.5	8.0	8.9
4	nan	6.0	4.5	5.0	4.4
5	nan	8.0	8.5	nan	nan

In Table 8.1, there are missing values in the target station dataset for days 2, 3, and 5. The missing value on day 2 will then be estimated with the data of the neighboring stations Y1, Y3, and Y4 since station Y2 is also missing a value on this day. All neighboring stations will be used for the estimation of the missing value on day 4, while only stations Y1 and Y2 have data available for the estimation of the missing value on day 5.
Since the number of neighboring stations with available data is not fixed in time, it is not possible to use a single MLR model to fill all the missing values for the target station all at once. For each missing value in the target station dataset, the program keeps only the datasets of the neighboring stations that also have data at this particular time. Data series of stations that do not respect the cutoff criteria for distance and elevation differences are also ignored. Data from neighboring stations are selected in descending order of their correlation coefficient with the target station, up to a maximal number of stations defined in the method parameters. The default value for the maximal number of neighboring station was set to four, based on the literature (Eischeid et al., 1995; Xia
et al., 1999).

41
If for a given day, no neighboring stations have a measured value to fill a gap in the target station dataset, no calculation is done and a ‘‘NaN’’ value is kept in the series instead and the program pass to the next missing value in the target series. An estimated (filled) value cannot be used to fill gaps of other station datasets.???

#### Multiple Linear Regression Model
First, the program will be checking if the sequence of neighboring stations has already been encountered for the current weather variable and, if so, will load the MLR parameters from memory and will directly estimate the missing value. Otherwise, the model will generate a new MLR model using either an Ordinary Least Square (OLS) or a Least Absolute Deviations (LAD) criteria (both options are available in the module?).
Since daily precipitation series generally have a positively-skewed distribution, the LAD criterion is typically a better option than the OLS criteria for handling this kind of distribution because it is more robust to outliers (Eischeid et al., 2000, 1995). The downside is an increase in computation time. The MLR using a LAD criterion is computed in WHAT with an iterative reweighted least-squares method (Schlossmacher, 1973; (Eischeid et al., 1995).

#### Estimating Missing Daily Values
When the parameters of the MLR model for a given day with a missing value are known, the missing value in the target time series is estimated as:

N
X(t) = a0 + )"' ai · Yi(t)	(8.1)
i=1

where X(t) is the missing value of the target station estimated at time t, Yi are the synchronous values of the neighboring stations, ai are the regression coefficients and N is the total number of neighboring stations used for the regression, up to the maximal value defined in the method (default is four).
When all missing values in the target station dataset have been estimated, the resulting gap free time series is saved in a ‘‘.out’’ file. Detailed information about the estimated values are saved in an accompanying ‘‘.log’’ file (see Section 8.3.1).

### Step 3: Validation
WHAT also includes an option to perform a validation of the method used for a particular weather dataset with a jackknife procedure. This option is an advanced feature that can be activated by changing the value of the field ‘‘Full Error Analysis’’ from 0 to 1 in the file named ‘‘WHAT.pref’’ (see Section 8.3.1).
More specifically, when this option is activated, WHAT will estimate a value for the target station for every day of the time series. In other words, loop B in the flowchart of Figure 8.1 will run over all the days of the dataset and not only over days for which there is a missing data. In addition, the memory feature will be deactivated and a MLR model will be estimated for each day independently. If a measured value is present for the current day being estimated, this value will be temporarily discarded from the data series to avoid self-influence of the observation on the estimation procedure. Je ne comprends pas bien comment tu fais ton jacknife. Est-ce que tu le fais en utilisant 1 à 4 valeurs des stations avoisinantes pour les jours où il y a des données observées à la station sélectionnée, et tu compares la « vraie » observation à l’estimation? Ce n’est pas clair.
Consequently, the activation of this feature will significantly raise the computation time for filling the gaps in weather time series and should be used only when a detailed analysis of the estimation errors is required. The default information provided in the ‘‘.log’’ should contain sufficient material to fill the needs of a large number of projects. Thus, this process leads to the production of a weather time-series for which every value has been estimated in WHAT. The results are saved in a tsv (tab-separated values) text file with the extension ‘‘.err’’ that is named after the station name and ID similarly to the ‘‘.log’’ and ‘‘.out’’ files.
The accuracy of the estimation technique can then be assessed by comparing the estimated weather data with the respective non-missing observations in the original weather data file. There is currently no tool provided in WHAT to directly analyze the results from the Jackknife procedure. However, all the source code that has been written? for the production of the figures of Section 8.4 can be downloaded freely on GitHub at (https://github.com/jnsebgosselin/WHAT).