Creation of Gapless weather data series

    1. Searching for Stations
To start searching for weather stations in the online CDCD, go in the Download Data tab and click on the small magnifying glass icon located next to the Weather Station drop down list, which should be empty if you have just created a new project. This will open a new dialog window (see Figure 3.2) where you can search for stations located within a given radius around a geographical coordinate defined in latitude and longitude in decimal degrees. It is possible to further narrow down the search by including only stations that have data within a given period.
Clicking on the button Search initiates the search for weather stations with the specified parameters. The results are saved in the ‘‘‘weather stations.lst’’ file and the Weather Station drop down list is updated to list all the stations found during the search.

Figure 3.2: Graphical interface to the online CDCD database.

Alternatively, it is possible to use a custom list of Canadian stations generated manually without using the graphical interface. This is done by retrieving station information from their unique url directly on the government of Canada website (www.climate.weather.gc.ca). The information must be saved in a TSV text file with the ‘‘.lst’’ extension. The list can be loaded in WHAT by clicking on the small folder icon located next to the Weather Station drop down list. A detailed example is presented for the Marieville weather station in Appendix A.

    1. Data Downloading
Once a list of weather stations has been generated in WHAT, either by an automatic search with the interface or manually, data can be downloaded from the online CDCD by selecting the desired station in the drop-down menu list and clicking on the Get Data button. WHAT will automatically download daily weather data from the CDCD for each year specified by the user in the Download Data year range and save the results as a CSV file in the Raw binder? (see section 2.4).
The downloading process can be stopped at any time by clicking on the button Get Data which will then be displaying a red stop icon. Before downloading the data for a given year, WHAT will first check if data already exist in the Raw binder. If it is the case, data for this year won’t be downloaded and the process will proceed? to the following year, otherwise data will be downloaded and saved. Detailed information about the program transactions during the downloading process are printed in the console area located at the bottom of the interface (see section 1.3).

Data Formatting
As soon as a downloading task successfully ends for a given weather station, WHAT automatically formats and concatenates the data. To do this, data from each annual file are put together end to end in chronological order and only data related to air temperature (mean, max and min) and total precipitation are kept. In addition, “NaN” (not a number)is entered where data are missing. Finally, statistics on the missing values in the dataset for each meteorological variable will be displayed in the Concatenated and Formatted Raw Data Files section.
By default, WHAT will automatically save the formatted data series in a single TSV file within the Input binder (see section 2.4). You can save other copies of the formatted data set anywhere on your computer by clicking on the Save button. The automatic saving of formatted data series can be disabled by unchecking the Automatically save concatenated data option. It is also possible to open previously downloaded weather data files in WHAT by clicking on the Load button and selecting the desired files in the dialog window. WHAT will then automatically format and concatenate the data and save the results automatically if the Automatically save concatenated data option is checked. Alternatively, the formatted data series can be saved by clicking on the button Save.

  1. Gap filling of daily weather records
One of WHAT’s interesting utility is the automatic gap filling of daily weather data records. This feature is accessible from the Fill Data tab shown in Figure 3.3.

When starting WHAT or when a project is opened, the content of the Input folder will be scanned for formatted weather data files and the results will be displayed as a list of weather station names under the label Fill Data for Weather Station.
This station list will not be refreshed automatically if new data files are added to the Input folder. binder after the project has been opened. The button Refresh, located next to the list of stations, can be used for this purpose. Each time WHAT searches the Input binder for valid weather data files, it automatically computes statistics for the period over which data are available and for the number of missing data in the weather time-series and saves the results in the file named ‘‘weather datasets summary.log’’ (see section 2.4).
If the Input binder is not empty,

Selecting a station from the drop-down list will automatically initiate the computation of correlation coefficients between the data of the selected station and those of the remaining stations (herein called the neighboring stations). Horizontal distances and elevation differences are computed as well. The results are displayed in the view panel located on the right side of the interface. Correlation coefficients that fall below a value of 0.7 are displayed in red in the table. This is only meant as guidance for the user and has no impact on the gap filling procedure. Information about the number of missing values in the dataset of the selected weather station are also displayed.

The process used to fill the gaps in the selected weather station datasets can be started by clicking the Fill button located at the bottom of the left side-panel.

Each missing value is estimated with a multiple linear regression (MLR) model generated with the synchronous weather time series of the selected and neighboring stations. The routine uses data from the neighboring stations that are best correlated with the data of the selected station, up to the maximum number of stations defined by the user. For example, in Figure 3.3, the program would use neighboring stations with the best correlation coefficient values up to a maximum of 4 stations. If for a given date, all the neighboring stations have missing data synchronously with the selected station, a NaN value is kept in the dataset at this particular date.

Figure 3.3: ‘‘Fill Data’’ tab.

It has been demonstrated that the MLR method outperforms most of the commonly used techniques for the estimation of missing data in daily meteorological records (Eischeid et al., 2000; 1995; Xia et al., 1999). It is possible to select whether the MLR model is generated using Ordinary Least Squares (OLS) or a Least Absolute Deviations (LAD) criteria from the \emph{Regression Model} menu. A regression based on a LAD is more robust to outliers than a regression based on a OLS, but is more expensive in computation time.

In general, data correlation between two stations for a given meteorological variable will decreases as the differences in their altitude and distance increase. Therefore, it is also possible to specify a threshold for the distance and altitude difference. Neighboring stations exceeding either one of these thresholds will be excluded from the gap filling procedure. A value of 100 km for the distance and 350 m for the altitude difference are set as default values in the program, based on the studies by (Simolo et al., 2010; Tronci et al., 1986; Xia et al., 1999).

The gaps in the dataset for the period specified by the user in the left side-panel and the complete daily weather datasets will be automatically saved in a tsv (tabular-separated values) file with the extension ‘‘.out’’ in the Output folder (see section 2.4). The file is named after the weather station name, climate ID, and first and last year of the dataset.

For example, the resulting output file for the station named Marieville in Figure 3.3 would be ‘‘MARIEVILLE (7024627) 1980-2014.log’’. In addition, detailed information on the missing data estimated by WHAT to fill the gap in the data are saved in a file with the same name as the ‘‘.out”” file but with a ‘‘.log’’ extension. Information includes the number of stations used, station name and associated values (autre chose?).
It is also possible to run this procedure in batch mode to fill the gaps for the entire weather station list by clicking on the Fill All button. The parameters for the gap filling procedure will, however, be the same for all the stations.

if you want to fill the gaps in several station datasets at a time by clicking on the Fill All button. The parameters for the gap filling process will then be the same for all stations.

Uncertainty associated to the estimated missing values can be estimated with a cross-validation procedure. This is an advanced feature that is in an experimental stage and thus cannot presently be activated directly from the GUI. The activation of this feature can, however, be done by changing the value of the field ‘‘Full Error Analysis’’ from 0 to 1 in the file named ‘‘WHAT.pref’’ that is located within the ‘‘WHAT’’ folder (see Section 1.2). A software restart is required for this change to take effect. This feature is discussed in more details in Section 8. Activating this feature will significantly increase the computation time of the gap filling procedure, especially if the least absolute deviation regression model is selected, but will provide you interesting insights on the performance of the procedure for the different datasets.